# DRY SUIT SEAL REPAIR KIT

To effectively repair your garment you will first need to find a former to fit inside the wrist, ankle or neck of the garment (something like a bottle or better still a traffic cone!) This former must be a firm fit on the garment or no bond will be achieved.

The old seal will need to be removed from the garment and the area of old glue cleaned thoroughly with a degreaser (a bit of nail varnish remover/acetone on a cloth, then soapy water)

Rub the area of the glue lightly with sand paper on both surfaces to provide grip for the glue.

Allow both surfaces to become touch dry, align surfaces and carefully bring the two together pressing firmly to ensure all air bubbles are eliminated.

CARE MUST BE TAKEN TO ENSURE THAT THEY ARE ALIGNED BEFORE BRINGING THE SURFACES TOGETHER. - Once the two surfaces have touched they will not come apart without stretching the new seal.

Remove former and do not use for 48 hours to allow the glue to reach it’s full strength.