# Fitting The RS Vision Outhaul Replacement Plate

Supplied items:	New Outhaul Plate

Self Tapping Screws

3M Glue and Plunger

Tools Required	Pozi Screwdriver

Drill and 3mm Drill Bit (or smaller)

Allen key set

- The foredeck is held in place using inserted Machine screws and self tapping screws. The machine screws can be removed directly, as the threaded inserts are captive. Remove the self tapping screws.

- The furler line will need to be released from the cleat and the knot untied to allow the line to pull free once the foredeck is removed. Remember to re thread this before refitting the foredeck

- Slide the foredeck towards the transom and lift free so that the internal gubbins of the system are now in view.

- The spinnaker pole should now be visible. Pull this towards the transom to remove it from the tubular guide at the bow of the boat.

- The original outhaul plate should be removed entirely. If there are any large holes, which have been caused by the breakage of the original system, they should now be filled using the supplied 3M Glue. Curing time should be approximately half an hour.

- Now that the area is free of fittings the new plate can be applied. The plate itself may not be a perfect fit and could need some adjustment so that the tabs will fit snugly against the sidewalls of the foredeck recess.

- The plate should be fitted so that the curved section in the centre of the new fitting sits over the spinnaker pole tubular guide at the bow. Mark the position of the fixing holes onto the boat using a pencil or marker and the remove the fitting.

- Pilot holes at these points should now be drilled in preparation for the final fixing. Once drilled the new fitting can be screwed in using the new self tapping screws supplied.

- Refit the original outhaul block onto the deck loop attached to the new fitting. Once this has been done check the operation of the pole, once satisfied, the foredeck can be refitted.

DON’T FORGET TO RE-THREAD THE FURLER LINE!