# RS500 New Jib Tack

This is an addendum to section 4.7 of the manual:

Your boat has been fitted with a new style of Jib tack.

In order to fit it, first tie the end of the tack line onto the D ring on the sail, using a knot on a knot.

Take it through the shackle on the tack plate (on the boat) and back up through the cleat on the sail.

Finish off by tying a stopper knot in the end of the tack line.

The picture below shows the finished arrangement: